## Slide 1
Recycling of Lead-acid batteries are the environmental
success story of our time.
Recycling
Battery
Car
Basel Convention

## Slide 2: Contents
Introduction
Lead poisonous
UAE Responsibility
Factory Responsibility
Conclusion
The results

## Slide 3: Factory Vision
To Keep Environment Clean

## Slide 4: Similar Projects
Region | No
Europe | 32
America | 11
Asia | 9
Africa | 1

## Slide 5: Lead Poisonous

## Slide 6: Battery Components
Electrolyte H2SO4 15-25 %
Lead sulphate PbSO4 25-35 %
Lead oxide PbOx 8-15 %
Grid metals 20-30 %
Polypropylene 4-7 %
Heavy plastic, paper, fiber, 2 -7 %

## Slide 7: Collected batteries per year in UAE
Abu Dhabi emirate had over 784,000 cars at the end of 2011.
In 2011, the total number of vehicles registered in Dubai was 1,052,891. Out of this, more than 115,380 vehicles
Traffic congestion, the single biggest concern among Dubai's 1.44 million residents, The city has a car ownership rate of 541 cars per 1,000 population. If this trend continues, then by 2020, there will be 5.3 million registered cars in Dubai.
The total number of cars in UAE around 2.5 Millions

## Slide 8: Why Is Lead Harmful?
Lead gets into a person's system, it is distributed throughout the body just like helpful minerals such as iron, calcium, and zinc.
And lead can cause harm wherever it lands in the body.
In the bloodstream, for example, it can damage red blood cells and limit their ability to carry oxygen to the organs and tissues that need it, thus causing anemia.
Most lead ends up in the bone, where it causes even more problems.

## Slide 9: Effect of short - term lead poisoning
The short-term effects of lead poisoning include:
Acute fever,
Convulsions,
Loss of consciousness and blindness, with anemia,
Renal failure
Exposure to high levels of lead in a short period of time is called Acute toxicity.

## Slide 10: Effects of Long-Term Lead Poisoning
Decreased bone and muscle growth
Poor muscle coordination
Damage to the nervous system, kidneys, and/or hearing and brain damage.
Speech and language problems
Developmental delay
Seizures and unconsciousness (in cases of extremely high lead levels)
Exposure to small amounts of lead over a long period of time is called Chronic toxicity.

## Slide 11: Signs of Lead Poisoning
Many kids with lead poisoning don't show any signs of being sick, so it's important to eliminate lead risks at home and to have young kids tested for lead exposure.
When kids do develop symptoms of lead poisoning, they usually appear as:
Irritability or behavioral problems (eating of no nutritious things such As dirt and paint chips)
Difficulty concentrating - headaches
Loss of appetite - weight loss
Sluggishness or fatigue - abdominal pain
Vomiting or nausea - constipation
Pallor (pale skin) from anemia - metallic taste in mouth
Muscle and joint weakness or pain - seizures

## Slide 12: UAE Responsibility

## Slide 13: What about next generation???
Environmental Rights
Air Emissions and Ambient Air Quality
Energy Conservation
Wastewater and Ambient Water Quality
Water Conservation
Hazardous Materials Management
Waste Management
Noise
Contaminated Land and Remediation

## Slide 14: Factory Responsibility

## Slide 15: Pre-Recycling

## Slide 16: Pre-recycling Environ. Control

## Slide 17: Pre-Recycling Steps
Used batteries must be
Collected,
Transported
Stored with proper care,
in order to avoid adverse health effects and environmental contamination.

## Slide 18: Acid drainage
The drainage of this liquid may pose several threats to the human health and to the environment, the drainage at collection points it should be avoided;
Others
Safe Box

## Slide 19: Rain
the storage facility must be sheltered from rain and other water sources,
Save Box
Others

## Slide 20: Transporting
Used lead-acid batteries must be considered as hazardous wastes when transport is needed. drivers and auxiliaries should be trained and use PPE
Collection truck
Others

## Slide 21: Stored in proper places
the ideal place to store used lead-acid batteries is inside a acid-resistant container that may simply be sealed and used as the transport container as well minimizing the risk of an accidental spillage.
Storing Boxes
Others

## Slide 22
Recycling

## Slide 23: Plant Specifications
Electrolyte Collection and Filtration Unit
Breaker and Separation Unit
Lead paste Desulphurization &Filtration
Sodium Sulphate Production Unit
Gaseous Effluents Scrubbing System Unit
Lead Smelting Unit
Lead Refinery and casting Unit

## Slide 24: Process Description
Factory
CX Area
Smelting
Refinery
Casting
Gas Scrubber
Paste treat
Sulphate production
Electrolyte Collection
Lead
production
Plastic production

## Slide 25: Environmental Monitoring
Control measures ensure that operational mistakes and accidents are decreased as much as possible,
In a modern lead recycling plant, the cost of pollution treatment, including effluents, smoke and dusts removal, and elimination of sulphur dioxide (SO2), amounts to 20-30% of the investment costs.

## Slide 26: CX Area Environ. Control

## Slide 27: CX Area
Batteries breaking.
Components separation, and cleaning
Paste thickening.
Paste and sulphate solution filtration.
Sulphate solution evaporation.
Sodium sulphate crystallization.
Sodium sulphate centrifugation.
Sodium sulphate drying.

## Slide 28: Separation and Treatment

## Slide 29: Liquid and solid
Liquid
plant washing water , necessary for floor, spills and equipments washing can be recovered into the process. no process liquid effluent will be released from the plant.
Solid
excluding the by-products of process (ebonite , separators and others) no other solid effluent is released at the CX area.

## Slide 30
 | Locations |  |  |  |  |  |  |  |  | Others
1 | CX area | √ | √ | √ | √ | ----- | √ | √ | ----- | -----
 | Batteries Bunker | √ | √ | √ | √ | In case of handling Soda And Acid | √ | √ | In case of handling Soda And Acid | 
 | breaker | √ | √ | √ | √ |  | √ | √ |  | -----
 | Sulphate process | √ | √ | √ | √ |  | √ | √ |  | -----
2 | Inside factory gate | √ | √ |  |  | ----- | ----- | ----- | ----- | -----
Personnel protective equipments in Factory

## Slide 31: Factory
factory
Others

## Slide 32: Process
Factory process
Others

## Slide 33: Wet Gas scrubber
Every source of pollutant gas effluents from:-
battery bunker
Battery breaking
Reactor
Conveyor and mill
For wet gas only.

## Slide 34: Unlicensed lead smelters
collectors must not sell their batteries to unlicensed lead smelters:
since unlicensed smelters are one of the main sources of lead contamination,
Good process area
Others

## Slide 35: Truck wash
truck wash
Others

## Slide 36: Smelting Area Environ. Control

## Slide 37
Smelting Area
Smelting involves the reduction of lead-bearing scrap into metallic lead in a furnace.
Lead and reagents are loaded in rotary furnace with the highest Possible mixing grade .
For small furnace loads and whenever be possible, it is advisable To mix the feed components (lead and reagents) before loading them Into the furnace.

## Slide 38: Gas scrubber
Every source of pollutant gas effluents from:-
Furnace
Kettles
Casting
Slag
For dry gas only
No. | Pollutant | Range | Unit
1 | Total dust | 5.0 | mg/ Nm3
2 | Lead | 0.5 | mg/Nm3
4 | Temperature | 40 - 50 | 0C

## Slide 39: Ventilated Furnace
Advanced Furnace
Others

## Slide 40
Gas scrubber
Flue gases from furnaces and air from ventilation systems are vented to cyclones, scrubbers, bag houses, etc. for particulate removal.
Flue dust must be removed from the separator (air pollution control equipment) and transported to storage, recycle streams, or to off-plant receivers.
Dust collection systems can be a significant source of lead exposure if not properly operated, cleaned, and maintained.

## Slide 41
Air filter bag house
“Air Filter Bag House”
contains 100% polyester Non-woven fabric filter bags fitted in the bag holding cage.
The bag house is equipped with pulse jet type cleaning arrangement.
Pulsejet cleaning unit is designed for continuous operation that operates at appropriate pressure of compressed dry air.

## Slide 42: Refinery Area Environ. Control

## Slide 43: Refinery Area
The objective of the refining process is to remove almost all of:-
Copper (Cu)
Antimony (Sb)
Arsenic (As)
Tin (Sn)
since soft lead are not allowed to have more than 10g per ton of these metals.

## Slide 44
Gas scrubber
Flue gases from furnaces and air from ventilation systems are vented to cyclones, scrubbers, bag houses, etc. for particulate removal.
Flue dust must be removed from the separator (air pollution control equipment) and transported to storage, recycle streams, or to off-plant receivers.
Dust collection systems can be a significant source of lead exposure if not properly operated, cleaned, and maintained.

## Slide 45
Air filter bag house
“Air Filter Bag House”
Contains 100% polyester Non-woven fabric filter bags fitted in the bag holding cage.
The bag house is equipped with pulse jet type cleaning arrangement.
Pulsejet cleaning unit is designed for continuous operation that operates at appropriate pressure of compressed dry air.

## Slide 46: Safe Work Environmental
ventilated process area
Others

## Slide 47: Casting Area Environ. Control

## Slide 48: Casting
Refined, or alloyed lead is pumped via heated pipes from kettles to a casting reservoir, or casting wheel, which directs a measured amount of lead into steel or cast iron molds.
Hand operations include drossing and stacking cooled castings.

## Slide 49: Lead ingots
Refining Process we churn out Pure Lead Ingots with a minimum purity level of 99.97% by weight that in mostly achieves purity level of 99.985%.
Elements | Composition in % | 
Antimony (Sb) | 0.001 (max) | 
Arsenic (As) | 0.001 (max) | 
Tin (Sn) | 0.001 (max) | 
Copper (Cu) | 0.001 (max) | 
Bismuth (Bi) | 0.030 (max) | 
Iron (Fe) | 0.001 (max) | 
Nickel (Ni) | 0.001 (max) | 
Silver (Ag) | 0.005 (max) | 
Zinc (Zn) | 0.001 (max) | 
Calcium (Ca) | 0.0005 (max) | 
Sulphur (S) | 0.0005 (max) | 
Aluminum (Al) | 0.0005 (max) | 
Lead (Pb) | 99.980 (min | 

## Slide 50: Lab. Environ. Control

## Slide 51: Most Advanced Laboratory
Optical Emission Spectrometer
Atomic Absorption Spectrometer

## Slide 52: Most Advanced Laboratory
Air Analyzer
CHNS Analyzer

## Slide 53: work practices
Prohibit smoking in the working place;
Segregate the work and eating areas;
Enforce showering at the end of work;
Change out of work clothes before going home;
Change and launder work wear daily;
Check and clean respirators daily.

## Slide 54: Conclusion
What would be happened if there is not technology likes?

## Slide 55: Old Technology
Environmental Advantages of Battery Recycling by New Technologies:
There is no solid wastes for land filling.
Protection for the following:
  Soil
  Air
  Ground water
  Safety for human health
  Safety for marine
  Safety for animal

## Slide 56: Polluted Soil
Damage of environmental quality.
Damage of population health.
Destroy of reuse and recycle as means to
protect non-renewable natural resources.
Damage of a sustainable and regulated system of lead utilization.

## Slide 57
Polluted Soil
Lead poisoning does not affect just people, it also affects the environment. The toxic metal is not able to dissolve in water or biodegrade, dissipate, decay, or burn.
This makes lead an extremely harmful hazard.
The lead that gets into the soil ends up staying there for a long time since it does not break down.

## Slide 58: Polluted Air
The air will pollute by:-
1- Acid mist, causing acid rain and damage the environment.
Acid rain contains more pH than ordinary.
This is caused by the presence of air pollutants, like sulfur dioxide and nitrogen oxides.
Acid rain is considered as the wet deposits of air pollutants,
2- Lead particles pollution of environment

## Slide 59: Polluted Water
Damage of environmental quality.
Damage of population health.
Destroy of reuse and recycle as means to
protect non-renewable natural resources.
Damage of a sustainable and regulated system of lead utilization

## Slide 60
Polluted groundwater
Plume is an underground pattern of contaminant concentrations created by the movement of groundwater beneath a contaminant source, with the contaminants spreading in the direction of groundwater movement. The source site has the highest concentration, and the concentration decreases and dissipates away from the source.

## Slide 61: Suffering of Some peoples

## Slide 62: The results
Environmental Damage
Mother earth

## Slide 63
Thanks
Gamal A. Hamid
gamal_a_hamid@hotmail.com